## Slide 1: Pilot Study on Automated Sphygmomanometers Accuracy Subject Expert for Medical Measurements
Presented by:
Jin-Hai Yang,
Dr. Cheng-Tsair Yang
Bureau of Standards, Metrology and Inspection
Chinese Taipei

## Slide 2
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Outline
Ⅰ. Initiative
Ⅱ. Project
Ⅲ. Implementation Method
Ⅳ. Relative activity

## Slide 3: Initiative-1
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
The most common methods to measure the blood pressure：
  Auscultatory method,
  Oscillometric method.

## Slide 4
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Initiative-2
Auscultatory method and sphygmomanometers applied(OIML R 16-1):
Mercury Column Type
Aneroid Type

## Slide 5
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Disadvantage:
  Well trained & experienced physician required.
  Fatigue.
  Fail to identify Korotkoff sounds
Initiative-3

## Slide 6
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Oscillometric method and sphygmomanometers applied(OIML R 16-2):
Initiative-4
Wrist Type
Upper Arm Type

## Slide 7
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Test items of Initial Verification:
  the maximum permissible errors of the cuff pressure indication,
  the influence of temperature on cuff pressure indication,
  the effect of voltage variations of the power source on the cuff pressure indication,
  the effect of voltage variations of the power source,
  air leakage of the pneumatic system.
Initiative-5

## Slide 8
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Initiative-6

## Slide 9
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Initiative-7

## Slide 10
Title: Pilot Study on Automated Sphygmomanometer Accuracy Test Using Blood Pressure Simulation Technique/APMP MMFG INITIATIVE PROJECT
Duration: June 01, 2018~December 31,2019
Participate Economies:
  P.R. China,
  Rep. Korea,
  Chinese Taipei.
Project-1
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019

## Slide 11
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
The main purpose:
  to establish an ISO/IEC 81060 compliant method for evaluating/testing the accuracy of automated sphygmomanometers using real human blood pressure (BP) simulation technique,
  to develop an APMP regional guideline for accuracy test of automated sphygmomanometers using blood pressure simulation system.
Project-2

## Slide 12
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Kick off meeting
Held at KRISS on 6-7 September 2018,
Six delegates attended:
  Dr. Sheng-Jui Chen from CMS/ITRI,
  Dr. Yong-Tae Kim and Dr. Il Doh from KRISS,
  Dr. Ding Xiang and Dr. Hu Zhixiong from NIM,
  Dr. Ashok Kumar from CSIR-NPL.
Introduction of each NMI’s BP simulation development,
Discussion on the draft protocol for BP simulation pilot study:
  Standardize the waveform format,
  Exchange waveforms for comparison,
  Verify the feasibility of BP accuracy evaluation using NIBP simulator.
Project-3

## Slide 13
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
2nd MMFG FGI Project Workshop
Held at NIM on 9-12 September 2019,
Participating Economies:
  India, Philippines, P.R. China, Rep. Korea, Chinese Taipei.
Progress report of FGI:
  Protocol of Pilot Study on Automated Sphygmomanometer Accuracy Test by Using Blood Pressure Simulation Technique_v3,
  Results of BP simulation pilot study.
Discussion on related topics:
  BP clinical data collection demonstration,
  Continuous non-invasive sphygmomanometers .
Project-4

## Slide 14
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Protocol of the pilot study
Measurement procedure,
Part I: characterize the basic capabilities of the participant’s blood pressure simulation system:
  Accuracy of the static pressure,
  Accuracy of the pulse rate,
  Repeatability of the oscillation amplitude,
  Repeatability of the oscillation shape.
Part II: accuracy test of two commercial NIBP oscillometric devices.
Project-5

## Slide 15
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
International standards:
  (i) ISO 81060-2:2018 Non-invasive sphygmomanometers --Part 2: Clinical investigation of automated measurement type,
  (ii) EN 1060-4:2004 Non-invasive sphygmomanometers. Test procedures to determine the overall system accuracy of automated non-invasive sphygmomanometers.
Implementation Method-1

## Slide 16
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Participants produce BP waveform data by their own blood pressure simulation system (BPSS) to check:
  (i) the data compatibility with the BPSS,
  (ii) consistency between original and regenerated BP waveforms (this will reference a new draft ISO standard),
  (iii) the correctness of systolic and diastolic BP values regenerated by the BPSS.
Implementation Method-2

## Slide 17
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
  Comparison with an auscultatory reference sphygmomanometer(Same arm simultaneously method):
  1.Tested device( simulator),
  2.Reference manometers,
  3.Double stethoscopes.
Implementation Method-3

## Slide 18
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
CMS/ITRI’s Human BP simulator
  The simulator is programmed to produce small oscillometric pulses according to the extracted oscillometric pulses and the instantaneous pressure inside the cuff.
Pulse Generator
Cuff
Mandrel
NIBP Device
T-Piece connector
Hose
Implementation Method-4

## Slide 19
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Original idea for the Pilot Study
Reference BP waveform BP Simulators Results
database
KRISS BP Waveforms
KRISS BP Waveforms
Systolic & diastolic pressures
CMS/ITRI BP Waveforms
CMS/ITRI BP Simulator
Systolic & diastolic pressures
Implementation Method-5

## Slide 20
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
    APLMF MEDEA 2.0 in medical metrology field
    Title: Training Course on Calibration & Testing on Non-Invasive Sphygmomanometers,
Duration: November 11~15, 2019.
Objective: To improve the metrological traceability of non- invasive sphygmomanometer and the legal metrological control of the device after the market.
This training course was requested by participant during the MEDEA 2.0 workshop on July 3-6 2018 in Hong Kong.
Relative Activity-1

## Slide 21
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Achievement: To provide developing economies’ metrological staff:
  to have basic knowledge of legal metrology, medical metrology and blood pressure measurement technique,
  to establish the fundamental background of the global regulations of non-invasive sphygmomanometer,
  to establish the technology of how to calibration and testing non-invasive sphygmomanometer,
  to understand the linkage between scientific metrology and legal metrology of non-invasive sphygmomanometer.
Relative Activity-2

## Slide 22
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
    Host: National Metrology Institute of Malaysia.
    Venue: Concorde Hotel Shah, Kuala Lumpur,
Trainer:
  Dr. Stephan Mieke (PTB retire, ISO expert),
  Mr. Chen Chuan Hung (CMS/ITRI), Co-Trainer: Mr Mazid Mansur (NMIM).
Relative Activity-3

## Slide 23
26th APLMF
Ha Long City, Viet Nam
7-9 November 2019
Thanks for your attention!
The end